TECPEL CO., LTD.  http://www.tecpel.com

Tel: 886-2-2737-5866 Fax: 886-2-2737-3343 E-mail: sales@tecpel.com

TR-51A  & TR-52  Specification Sheet

|  | TR-51A | TR-52 |
| --- | --- | --- |
| Measurement Channel | 1 Temperature Channel | 1 Temperature Channel |
| Internal Sensor | -40 to 80°C | - |
| External Sensor | - | -60 to 155°C |
| Measurement Accuracy | ±0.5°C | Average ±0.3°C (-20 to 80°C) Average ±0.5°C (-40 to -20°C / 80 to 110°C) Average ±1.0°C (-60 to -40°C / 110 to 155°C) |
| Measurement Resolution Display | 0.1°C |
| Sensor | Thermistor |
| Recording Interval | 1,2,5,10,15,20,30,60 minutes (8 variations) | 1,2,5,10,15,20,30 seconds / 1,2,5,10,15,20,30,60 minutes (15 variations) |
| Recording Capacity | 16,000 Readings x 1 Channel |
| Measurement method*1 | Endless loop method (Overwrite from the oldest data when recording capacity is full) One Time Method (Stop recording when recording capacity is full) |
| LCD display | Current Temperature, Recording Condition, Battery Life Warning, and Unit of Temperature (°F and °C) |
| Battery | Lithium battery (ER3V M) x 1 (Also availabe with CR2) |
| Battery Life *2 | Approximately 2 years | Maximum 2 years |
| Interface | Optical Communication (Between a Unit and TR-50C) |
| Communication Speed | 2,400bps (Communication Period of 3 minutes or less) |
| Water Resistance Capacity *3 | IP67 | IP64 *4 |
| Dimensions | H62mm x W47mm x D19mm |
| Weight | 53g (Including battery) | 55g (Including battery) |
| Temperature Resistance of Unit | -40 to 80°C |
| Standard Sensor | Built-in | TR-5106: (Teflon resin sensor) |
| *1 Lithium Battery (CR-2) can be used for this unit, however the possible temperaure mesurement will be - 20 to 60°C. If you are measuring below -20°C or above 60°C, we recommend the Optional Battery Set TR-00P2 *2 Battery Life differs depending on measurement environment and battery performance. *3 Not for continued immersion. *4 The water resistance rating with the sensor or input cable connected is IP64 |